## Slide 1: Assembly Language for x86 Processors 6th Edition
Chapter 1: Introduction to ASM
(c) Pearson Education, 2010. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Slides prepared by the author
Revision date: 2/15/2010
Kip Irvine

## Slide 2: The Bottom-Up Approach
We can study computer architectures by starting with the basic building blocks
  Transistors and logic gates
To build more complex circuits
  Flip-flops, registers, multiplexors, decoders, adders, ...
From which we can build computer components
  Memory, processor, I/O controllers…
Which are used to build a computer system
This was the approach taken in your first course 03-60-265: Computer Architecture I: Digital Design

## Slide 3: The Top-Down Approach
In this course we will study computer architectures from the programmer’s view
We study the actions that the processor needs to do to execute tasks written in high level languages (HLL) like C/C++, Pascal, …
But to accomplish this we need to:
  Learn the set of basic actions that the processor can perform: its instruction set
  Learn how a HLL compiler decomposes HLL command into processor instructions

## Slide 4: The Top-Down Approach (Ctn.)
We can learn the basic instruction set of a processor either
  At the machine language level
    But reading individual bits is tedious for humans
  At the assembly language level
    This is the symbolic equivalent of machine language (understandable by humans)
Hence we will learn how to program a processor in assembly language to perform tasks that are normally written in a HLL
  We will learn what is going on beneath the HLL interface

## Slide 5: Welcome to Assembly Language
How does assembly language (AL) relate to machine language?
How do C++ and Java relate to AL?
Is AL portable?
Why learn AL?

## Slide 6: Levels and Languages
The compiler translates each HLL statement into one or more assembly language instructions
The assembler translate each assembly language instruction into one machine language instruction
  Each processor instruction can be written either in machine language form or assembly language form
  Example, for the Intel Pentium:
    MOV AL, 5 ;Assembly language
    10110000 00000101 ;Machine language
Hence we will use assembly language
High-level
language
program
Assembly
language
program
Machine
language
program
Compiler
Assembler

## Slide 7: Translating Languages
English: Display the sum of A times B plus C.
C++: cout << (A * B + C);
Assembly Language:
Mov eax,A
Mul B
Add eax,C
Call WriteInt
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000

## Slide 8: Assembly Language Today
A program written directly in assembly language has the potential to have a smaller executable and to run faster than a HLL program
But it takes too long to write a large program in assembly language
  Only time-critical procedures are written in assembly language (optimization for speed)
Assembly language are often used in embedded system programs stored in PROM chips
  Computer cartridge games, micro controllers, …
Remember: you will learn assembly language to learn how high-level language code gets translated into machine language
  i.e. to learn the details hidden in HLL code

## Slide 9: Comparing ASM to High-Level Languages

## Slide 10: Specific Machine Levels
(descriptions of individual levels follow . . . )

## Slide 11: High-Level Language
Level 4
  Application-oriented languages
  C++, Java, Pascal, Visual Basic . . .
  Programs compile into assembly language (Level 3)

## Slide 12: Assembly Language
Level 3
  Instruction mnemonics that have a one-to-one correspondence to machine language
  Programs are translated into Instruction Set Architecture Level - machine language (Level 2)
To be learned in 03-60-266

## Slide 13: Instruction Set Architecture (ISA)
Level 2
  Also known as conventional machine language
  Executed by Level 1 (Digital Logic)
    The hardware (taught in 03-60-265)

## Slide 14: Digital Logic
Level 1: the digital system seen in 03-60-265
  CPU, constructed from digital logic gates
  System bus
  Memory
  Implemented using bipolar transistors

## Slide 15: Basic Microcomputer Design
Central Processor Unit:
  clock synchronizes CPU operations
  control unit (CU) coordinates sequence of execution steps
  ALU performs arithmetic and logic operations
Bus: transfer data between different parts of the computer
  Data bus, Control bus, and Address bus

## Slide 16: Review: Data Representation
Binary Numbers
  Translating between binary and decimal
Binary Addition
Integer Storage Sizes
Hexadecimal Integers
  Translating between decimal and hexadecimal
  Hexadecimal subtraction
Signed Integers
  Binary subtraction
Character Storage

## Slide 17: Memory Units for the Intel x86
The smallest addressable unit is the BYTE
  1 byte = 8 bits
For the x86, the following units are used
  1 word = 2 bytes
  1 double word = 2 words (= 32 bits)
  1 quad word = 2 double words

## Slide 18: Data Representation
To obtain the value contained in a block of memory we need to choose an interpretation
Ex: memory content 0100 0001 can either represent:
  The number
  Or the ASCII code of character “A”
Only the programmer can provide the interpretation

## Slide 19: Number Systems
A written number is meaningful only with respect to a base
To tell the assembler which base we use:
  Hexadecimal 25 is written as 25h
  Octal 25 is written as 25o or 25q
  Binary 1010 is written as 1010b
  Decimal 1010 is written as 1010 or 1010d
You already know how to convert from one base to another (if not, review your 03-60-265 class notes)

## Slide 20: Binary Numbers
Digits are 1 and 0
  1 = true
  0 = false
MSB – most significant bit
LSB – least significant bit
Bit numbering:

## Slide 21: Binary Numbers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:
Every binary number is a sum of powers of 2

## Slide 22: Translating Binary to Decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
dec = (Dn-1  2n-1) + (Dn-2  2n-2) + ... + (D1  21) + (D0  20)
D = binary digit
binary 00001001 = decimal 9:
(1  23) + (1  20) = 9

## Slide 23: Translating Unsigned Decimal to Binary
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:
37 = 100101

## Slide 24: Binary Addition
Starting with the LSB, add each pair of digits, include the carry if present.

## Slide 25: Integer Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 26: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 27: Translating Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer 000101101010011110010100 to hexadecimal:

## Slide 28: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16:
  dec = (D3  163) + (D2  162) + (D1  161) + (D0  160)
Hex 1234 equals (1  163) + (2  162) + (3  161) + (4  160), or decimal 4,660.
Hex 3BA4 equals (3  163) + (11 * 162) + (10  161) + (4  160), or decimal 15,268.

## Slide 29: Powers of 16
Used when calculating hexadecimal values up to 8 digits long:

## Slide 30: Converting Decimal to Hexadecimal
decimal 422 = 1A6 hexadecimal

## Slide 31: Hexadecimal Addition
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.
36 28 28 6A
42 45 58 4B
78 6D 80 B5
1
1
21 / 16 = 1, rem 5
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.

## Slide 32: Hexadecimal Subtraction
When a borrow is required from the digit to the left, add 16 (decimal) to the current digit's value:
C6 75
A2 47
24 2E
-1
16 + 5 = 21
Practice: The address of var1 is 00400020. The address of the next variable after var1 is 0040006A. How many bytes are used by var1?

## Slide 33: Integer Representations
Two different representations exists for integers
The signed representation: in that case the most significant bit (MSB) represents the sign
  Positive number (or zero) if MSB = 0
  Negative number if MSB = 1
The unsigned representation: in that case all the bits are used to represent a magnitude
  It is thus always a positive number or zero

## Slide 34: Signed Integers
The highest bit indicates the sign. 1 = negative, 0 = positive
If the highest digit of a hexadecimal integer is > 7, the value is negative. Examples: 8A, C5, A2, 9D

## Slide 35: Forming the Two's Complement
Negative numbers are stored in two's complement notation
Represents the additive Inverse
Note that 00000001 + 11111111 = 00000000

## Slide 36: Binary Subtraction
When subtracting A – B, convert B to its two's complement
Add A to (–B)
0 0 0 0 1 1 0 0 0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1
0 0 0 0 1 0 0 1
Practice: Subtract 0101 from 1001.

## Slide 37: Learn How To Do the Following:
Form the two's complement of a hexadecimal integer
Convert signed binary to decimal
Convert signed decimal to binary
Convert signed decimal to hexadecimal
Convert signed hexadecimal to decimal

## Slide 38: Ranges of Signed Integers
The highest bit is reserved for the sign. This limits the range:
Practice: What is the largest positive value that may be stored in 20 bits?

## Slide 39: Signed and Unsigned Interpretation
To obtain the value of a integer in memory we need to chose an interpretation
Ex: a byte of memory containing 1111 1111 can represent either one of these numbers:
  -1 if a signed interpretation is used
  255 if an unsigned interpretation is used
Only the programmer can provide an interpretation of the content of memory

## Slide 40: Maximum and Minimum Values
The MSB of a signed integer is used for its sign
  fewer bits are left for its magnitude
Ex: for a signed byte
  smallest positive = 0000 0000b
  largest positive = 0111 1111b = 127
  largest negative = -1 = 1111 1111b
  smallest negative = 1000 0000b = -128
Exercise 2: give the smallest and largest positive and negative values for
  A) a signed word
  B) a signed double word

## Slide 41: Character Representation
Each character is represented by a 7-bit code called the ASCII code
ASCII codes run from 00h to 7Fh (h = hexadecimal)
  Only codes from 20h to 7Eh represent printable characters. The rest are control codes (used for printing, transmission…).
An extended character set is obtained by setting the most significant bit (MSB) to 1 (codes 80h to FFh) so that each character is stored in 1 byte
  This part of the code depends on the OS used
    For Windows: we find accentuated characters, Greek symbols and some graphic characters

## Slide 42: The ASCII Character Set
CR = “carriage return” (Windows: move to beginning of line)
LF = “line feed” (Windows: move directly one line below)
SPC = “blank space”

## Slide 43: Text Files
These are files containing only printable ASCII characters (for the text) and non-printable ASCII characters to mark each end of line.
But different conventions are used for indicating an “end-of line”
  Windows: <CR>+<LF>
  UNIX: <LF>
  MAC: <CR>
This is at the origin of many problems encountered during transfers of text files from one system to another

## Slide 44: Character Storage
Character sets
  Standard ASCII (0 – 127)
  Extended ASCII (0 – 255)
  ANSI (0 – 255)
  Unicode (0 – 65,535)
Null-terminated String
  Array of characters followed by a null byte
Using the ASCII table
  back inside cover of book

## Slide 45: Numeric Data Representation
pure binary
  can be calculated directly
ASCII binary
  string of digits: "01010101"
ASCII decimal
  string of digits: "65"
ASCII hexadecimal
  string of digits: "9C"
next: Boolean Operations

## Slide 46: Boolean Operations
NOT
AND
OR
Operator Precedence
Truth Tables

## Slide 47: Boolean Algebra
Based on symbolic logic, designed by George Boole
Boolean expressions created from:
  NOT, AND, OR

## Slide 48: NOT
Inverts (reverses) a boolean value
Truth table for Boolean NOT operator:
Digital gate diagram for NOT:

## Slide 49: AND
Truth table for Boolean AND operator:
Digital gate diagram for AND:

## Slide 50: OR
Truth table for Boolean OR operator:
Digital gate diagram for OR:

## Slide 51: Operator Precedence
Examples showing the order of operations:

## Slide 52: Truth Tables (1 of 3)
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: X  Y

## Slide 53: Truth Tables (2 of 3)
Example: X  Y

## Slide 54: Truth Tables (3 of 3)
Example: (Y  S)  (X  S)
Two-input multiplexer

## Slide 55: Summary
Assembly language helps you learn how software is constructed at the lowest levels
Assembly language has a one-to-one relationship with machine language
Each layer in a computer's architecture is an abstraction of a machine
  layers can be hardware or software
Boolean expressions are essential to the design of computer hardware and software

## Slide 56: 54 68 65 20 45 6E 64
What do these numbers represent?