## Slide 1: Assembly Language for x86 Processors 6th Edition
Chapter 4: Data Transfers, Direct Addressing, Arithmetic, and Irvine32 Link Library
(Includes Chapter 5, Sections 5.1--5.3.2)
(c) Pearson Education, 2010. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Slides prepared by the author
Revision date: 2/15/2010
Kip Irvine

## Slide 2: Instruction Format Examples
No operands
  stc ; set Carry flag
One operand
  inc eax ; register
  dec myByte ; memory
Two operands
  add ebx, ecx ; register, register
  sub myByte, 25 ; memory, constant
  add eax, 36 * 25 ; register, constant-expression
  All two-operand instructions are in the form
  OpCode Destination, Source

## Slide 3: Operand Types
Immediate – a constant integer (8, 16, or 32 bits)
  value is encoded within the instruction
  imm8, imm16, imm32 ex: ‘A’, -273, 1234ABCDh
Register – the name of a register
  register name is converted to a number and encoded within the instruction
  reg8, reg16, reg32, sreg ex: AL, BX, ECX, DS
Memory – reference to a location in memory
  memory address is encoded within the instruction, or a register holds the address of a memory location
  mem8, mem16, mem32, mem

## Slide 4: Instruction Operand Notation

## Slide 5: Direct Memory Operands
A direct memory operand is a named reference to storage in memory
The named reference (label) is automatically dereferenced by the assembler
.data
var1 BYTE 10h
.code
mov al,var1 ; AL = 10h
mov al,[var1] ; AL = 10h
alternate format
(to be discussed in a later chapter)

## Slide 6: Data Transfer Instructions MOV Instruction
.data
count BYTE 100
wVal WORD 2
.code
mov bl,count
mov ax,wVal
mov count,al
mov al,wVal ; error
mov ax,count ; error
mov eax,count ; error
Both operands must be of the same size
Move from source to destination. Syntax:
    MOV destination, source;
No more than one memory operand permitted
CS, EIP, and IP cannot be the destination
No immediate to segment moves

## Slide 7: On Sizes and Types
The type of an operand is given by its size (byte, word, double-word, …, etc)
Both operands of MOV must be of the same size
Type checking is done by the assembler at compile time
The type assigned to a mem operand is given by its data allocation directive (BYTE, WORD, …).
The type assigned to a reg operand is given by its size.
An imm source operand of MOV must fit into the size of the destination operand.

## Slide 8: Your turn . . .
.data
bVal BYTE 100
bVal2 BYTE ?
wVal WORD 2
dVal DWORD 5
.code
mov ds,45
mov esi,wVal
mov eip,dVal
mov 25,bVal
mov bVal2,bVal
Explain why each of the following MOV statements are invalid:
immediate move to DS not permitted
size mismatch
EIP cannot be the destination
immediate value cannot be destination
memory-to-memory move not permitted

## Slide 9: Zero Extension
mov bl,10001111b
movzx ax,bl ; zero-extension
movzx ah,bl ; illegal, size mismatch
Does not preserved the sign if src is negative
When you copy a smaller value into a larger destination, the MOVZX instruction fills (extends) the upper half of the destination with zeros.
The destination must be a register.

## Slide 10: Sign Extension
mov bl,10001111b
movsx ax,bl ; sign extension
movsx ah,bl ; illegal, size mismatch
The MOVSX instruction fills the upper half of the destination with a copy of the source operand's sign bit. Only used with signed integers.
The destination must be a register.

## Slide 11: XCHG Instruction
.data
var1 WORD 1000h
var2 WORD 2000h
.code
xchg ax,bx ; exchange 16-bit regs
xchg ah,al ; exchange 8-bit regs
xchg var1,bx ; exchange mem, reg
xchg eax,ebx ; exchange 32-bit regs
xchg var1,var2 ; error: two memory operands
mov ax,var1
xchg var2,ax
mov var1,ax
XCHG exchanges the values of two operands. At least one operand must be a register. No immediate operands are permitted.

## Slide 12: Direct-Offset Operands – Another Example
Let the data segment be:
    .data
    arrB BYTE 10h, 20h
    arrW WORD 1234h, 5678h
arrB+1 refers to the location one byte beyond the beginning of arrB and arrW+2 refers to the location two bytes beyond the beginning of arrW.
    mov al,arrB ; AL = 10h
    mov al,arrB+1 ; AL=20h (mem with displacement)
    mov ax,arrW+2 ; AX = 5678h
    mov ax,arrW+1 ; AX = 7812h ; little endian convention!
    mov ax,arrW-2 ; AX = 2010h
    ; negative displacement permitted

## Slide 13: Direct-Offset Operands
.data
arrayB BYTE 10h,20h,30h,40h
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov al,arrayB+1 ; AL = 20h
mov al,[arrayB+1] ; alternative notation, tbdl
mov ax,[arrayW+2] ; AX = 2000h
mov ax,[arrayW+4] ; AX = 3000h
mov eax,[arrayD+4] ; EAX = 00000002h
We can add a displacement to a memory operand to access a memory value without a name. That is, a constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.
1. Why doesn't arrayB+1 produce 11h?
2. mov ax,[arrayW-2] ; ??
3. mov eax,[arrayD+16] ; ??
What will happen when 1 and 2 run?

## Slide 14: Your turn. . .
Write a program that rearranges the values of three doubleword values in the following array as: 3, 1, 2.
  .data
  arrayD DWORD 1,2,3
Step 2: Exchange EAX with the third array value and copy the value in EAX to the first array position.
Step1: copy the first value into EAX and exchange it with the value in the second position.
mov eax,arrayD
xchg eax,[arrayD+4]
xchg eax,[arrayD+8]
mov arrayD,eax

## Slide 15: Exercise 2
Given the following data segment
    .data
    A SWORD 1234h,-1
    B SDWORD 55h,12345678h
Indicate if the following instruction is legal. If it is, indicate the value, in hexadecimal, of the destination operand immediately after the instruction is executed (please verify your answers with a debugger)
    MOV eax,A
    MOV bx,A+1
    MOV bx,A+2
    MOV dx,A+4
    MOV cx,B+1
    MOV edx,B+2

## Slide 16: Simple Arithmetic Instructions INC and DEC Instructions
Add 1, subtract 1 from destination operand
  operand may be register or memory
INC destination
    Logic: destination  destination + 1
DEC destination
    Logic: destination  destination – 1
INC and DEC affect all status flags except the CF flag

## Slide 17: INC and DEC Examples
Show the value of the destination operand after each of the following instructions executes:
.data
myByte BYTE 0FFh, 0
.code
mov al,myByte ; AL =
mov ah,[myByte+1] ; AH =
dec ah ; AH =
inc al ; AL =
dec ax ; AX =
FFh
00h
FFh
00h
FEFF

## Slide 18: ADD and SUB Instructions
ADD destination, source
  Logic: destination  destination + source
SUB destination, source
  Logic: destination  destination – source
  The CPU performs A + NEG(B) where NEG = 2CF operation
Same operand rules as for the MOV instruction
  Source remains unchanged
  Both operands must be of the same size
  Cannot be both mem operands at the same time
ADD and SUB affect all status flags

## Slide 19: Evaluate this . . .
We want to write a program that adds the following three bytes:
.data
myBytes BYTE 80h,66h,0A5h
What is your evaluation of the following code?
mov al,myBytes
add al,[myBytes+1]
add al,[myBytes+2]
What is your evaluation of the following code?
mov ax,myBytes
add ax,[myBytes+1]
add ax,[myBytes+2]
Any other possibilities?

## Slide 20: Evaluate this . . . (cont)
.data
myBytes BYTE 80h,66h,0A5h
How about the following code. Is anything missing?
movzx ax,myBytes
mov bl,[myBytes+1]
add ax,bx
mov bl,[myBytes+2]
add ax,bx ; AX = sum
Yes: Move zero to BX before the MOVZX instruction.

## Slide 21: NEG (negate) Instruction
.data
valB BYTE -1
valW WORD +32767
.code
mov al,valB ; AL = -1
neg al ; AL = +1
neg valW ; valW = -32767
Reverses the sign of an operand. Operand can be a register or a memory operand. This is equivalent to the 2’s Complement (2CF) operation discussed in 03-60-265.
Suppose AX contains –32,768 and we apply NEG to it. Will the result be valid?
NEG affects all status flags

## Slide 22: Flags Affected by Arithmetic
The ALU has a number of status flags that reflect the outcome of arithmetic (and bitwise) operations
  based on the contents of the destination operand
Essential status flags:
  Zero flag – set when destination equals zero
  Sign flag – set when destination is negative
  Carry flag – set when unsigned value is out of range (unsigned overflow)
  Overflow flag – set when signed value is out of range (signed overflow)
The MOV instruction never affects the flags.

## Slide 23: Signed and Unsigned Integers A Hardware Viewpoint
All CPU instructions operate exactly the same on signed and unsigned integers
The CPU cannot distinguish between signed and unsigned integers
YOU, the programmer, are solely responsible for using the correct data type with each instruction
  You are also responsible for determining/using the correct interpretation of the results of operations
Added Slide. Gerald Cahill, Antelope Valley College

## Slide 24: Overflow Flag and Carry Flag A Hardware Viewpoint
How the ADD instruction affects OF and CF:
  CF = (carry out of the MSB)
  CI = (carry in to the MSB)
  OF = CF XOR CI
How the SUB instruction affects OF and CF:
  NEG the source and ADD it to the destination
  CF = INVERT (carry out of the MSB)
  CI = INVERT (carry in to the MSB)
  OF = CF XOR CI
MSB = Most Significant Bit (high-order bit)
XOR = eXclusive-OR operation
NEG = Negate (same as SUB 0,source )
Notes: See Pages 28 and 32

## Slide 25: Carry Flag (CF)
The Carry flag is set when the result of an operation generates an unsigned value that is out of range (too big or too small for the destination operand).
mov al,0FFh
add al,1 ; CF = 1, AL = 00
; Try to go below zero:
mov al,0
sub al,1 ; CF = 1, AL = FF

## Slide 26: Your turn . . .
mov ax,00FFh
add ax,1 ; AX= SF= ZF= CF=
sub ax,1 ; AX= SF= ZF= CF=
add al,1 ; AL= SF= ZF= CF=
mov bh,6Ch
add bh,95h ; BH= SF= ZF= CF=
mov al,2
sub al,3 ; AL= SF= ZF= CF=
For each of the following marked entries, show the values of the destination operand and the Sign, Zero, and Carry flags:
0100h 0 0 0
00FFh 0 0 0
00h 0 1 1
01h 0 0 1
FFh 1 0 1

## Slide 27: Overflow Flag (OF)
The Overflow flag is set when the signed result of an operation is invalid or out of range.
; Example 1
mov al,+127
add al,1 ; OF = 1, AL = ??
; Example 2
mov al,7Fh ; OF = 1, AL = 80h
add al,1
The two examples are identical at the binary level because 7Fh equals +127. To determine the value of the destination operand, it is often easier to calculate in hexadecimal.

## Slide 28: A Rule of Thumb
When adding two integers, remember that the Overflow flag (OF) is only set when . . .
  Two positive operands are added and their sum is negative
  Two negative operands are added and their sum is positive
  Then we have signed overflow
What will be the values of the Overflow flag?
mov al,80h
add al,92h ; OF =
mov al,-2
add al,+127 ; OF =
1
0

## Slide 29: OF and CF Flags
Both types of overflow occur independently and are signaled separately by CF and OF
    mov al, 0FFh
    add al,1 ; AL=00h, OF=0, CF=1
    mov al,7Fh
    add al, 1 ; AL=80h, OF=1, CF=0
    mov al,80h
    add al,80h ; AL=00h, OF=1, CF=1
Hence: we can have either type of overflow or both of them at the same time

## Slide 30: NEG Instruction and the Flags
.data
valB BYTE 1,0
valC SBYTE -128
.code
neg valB ; CF = 1, OF = 0
neg [valB + 1] ; CF = 0, OF = 0
neg valC ; CF = 1, OF = 1
The processor implements NEG using the following internal operation:
SUB 0,operand
Any nonzero operand causes the Carry flag to be set.

## Slide 31: Your turn . . .
mov al,-128
neg al ; CF = OF =
mov ax,8000h
add ax,2 ; CF = OF =
mov ax,0
sub ax,2 ; CF = OF =
mov al,-5
sub al,+125 ; OF =
What will be the values of the given flags after each operation?
1 1
0 0
1 0
1

## Slide 32: Overflow Example
  mov ax,4000h
  add ax,ax ;AX = 8000h
Unsigned Interpretation:
  The sum of the 2 magnitudes 4000h + 4000h gives 8000h. This is the result in AX (the unsigned value of the result is correct). CF=0
Signed Interpretation:
  we add two positive numbers: 4000h + 4000h
  and have obtained a negative number!
  the signed value of the result in AX is erroneous. Hence OF=1

## Slide 33: Overflow Example
  mov ax,8000h
  sub ax,0FFFFh ;AX = 8001h
Unsigned Interpretation:
  from the magnitude 8000h we subtract the larger magnitude FFFFh
  the unsigned value of the result is erroneous. Hence CF=1
Signed Interpretation:
  We subtract -1 from the negative number 8000h and obtained the correct signed result 8001h. Hence OF=0

## Slide 34: Overflow Example
  mov ah,40h
  sub ah,80h ;AH = C0h
Unsigned Interpretation:
  we subtract from 40h the larger number 80h
  the unsigned value of the result is wrong. Hence CF=1
Signed Interpretation:
  we subtract from 40h (64) a negative number 80h (-128) to obtain a negative number
  the signed value of the result is wrong. Hence OF=1

## Slide 35: Exercise 3
For each of these instructions, give the content (in hexadecimal) of the destination operand and the CF and OF flags immediately after the execution of the instruction (verify your answers with a debugger).
  ADD AX,BX when AX contains 8000h and BX contains FFFFh.
  SUB AL,BL when AL contains 00h and BL contains 80h.
  ADD AH,BH when AH contains 2Fh and BH contains 52h.
  SUB AX,BX when AX contains 0001h and BX contains FFFFh.

## Slide 36: I/O on the Win32 Console
Our programs will communicate with the user via the Win32 console (the MS-DOS box)
  Input is done on the keyboard
  Output is done on the screen
Modern OS like Windows forbids user programs to interact directly with I/O hardware
  User programs can only perform I/O operation via system calls
For simplicity, our programs will perform I/O operations by using procedures or macros that are provided in the Irvine32.inc or Macros.inc files
  Follow the steps in http://www.kipirvine.com/asm/gettingStartedVS2012/index.htm to download these files as well as the compiler and the Visual Studio 2012 programming environment.
  These procedures/macros are calling C libraries functions like printf() which, in turn, are calling the MS-Windows Win32 API
  Hence, these I/O operations will be slow but simple to use

## Slide 37: Irvine32 Link Library (Chapter 5, Sections 5.1--5.3.2)
A file containing I/O and Win32 procedures that have been compiled into machine code
  constructed from one or more OBJ files
In general, To build a library, . . .
  start with one or more ASM source files
  assemble each into an OBJ file
  create an empty link library file (extension .LIB)
  add the OBJ file(s) to the library file, using the Microsoft LIB utility
Take a quick look at Irvine32.asm in the \Irvine\Examples\Lib32 folder.
You can download the Irvine.32 link library from http://www.kipirvine.com/asm/examples/index.htm

## Slide 38: Irvine32 Link Library
Irvine32.asm: Source codes of the library procedures
Irvine32.lib: Book’s Link library
Irvine32.inc: Procedure prototypes of the library
Macros.inc: Macro definitions
Assembler and Linker command options
ML -c AddSub.asm → AddSub.obj
Link AddSub.obj Irvine32.lib Kernel32.lib → AddSub.exe
See page 600 for ML and LINK command line options
Or… Use Visual Studio 2012, which does these 2 steps automatically

## Slide 39: Linking to a Library
Your programs link to Irvine32.lib using the linker command inside a batch file named make32.bat.
Notice the two LIB files: Irvine32.lib, and kernel32.lib
  the latter is part of the Microsoft Win32 Software Development Kit (SDK)
  Kernel32.dll: MS-Windows Dynamic Link Library

## Slide 40: Calling a Library Procedure
INCLUDE Irvine32.inc
.code
mov eax,1234h ; input argument
call WriteHex ; show hex number
call Crlf ; end of line
Call a library procedure using the CALL instruction. Some procedures require input arguments. The INCLUDE directive copies in the procedure prototypes (declarations).
The following example displays "1234" on the console:

## Slide 41: Irvine32 Procedures - Overview (1 of 5) (Read Chapter 5, Section 5.3)
CloseFile – Closes an open disk file
Clrscr - Clears console, locates cursor at upper left corner
CreateOutputFile - Creates new disk file for writing in output mode
Crlf - Writes end of line sequence to standard output
Delay - Pauses program execution for n millisecond interval
DumpMem - Writes block of memory to standard output in hex
DumpRegs – Displays general-purpose registers and flags (hex)
GetCommandtail - Copies command-line args into array of bytes
GetDateTime – Gets the current date and time from the system
GetMaxXY - Gets number of cols, rows in console window buffer
GetMseconds - Returns milliseconds elapsed since midnight

## Slide 42: Irvine32 Procedures - Overview (2 of 5)
GetTextColor - Returns active foreground and background text colors in the console window
Gotoxy - Locates cursor at row and column on the console
IsDigit - Sets Zero flag if AL contains ASCII code for decimal digit (0–9)
MsgBox, MsgBoxAsk – Display popup message boxes
OpenInputFile – Opens existing file for input
ParseDecimal32 – Converts unsigned integer string to binary
ParseInteger32 - Converts signed integer string to binary
Random32 - Generates 32-bit pseudorandom integer in the range 0 to FFFFFFFFh
Randomize - Seeds the random number generator
RandomRange - Generates a pseudorandom integer within a specified range
ReadChar - Reads a single character from standard input

## Slide 43: Irvine32 Procedures - Overview (3 of 5)
ReadDec - Reads 32-bit unsigned decimal integer from keyboard
ReadFromFile – Reads input disk file into buffer
ReadHex - Reads 32-bit hexadecimal integer from keyboard
ReadInt - Reads 32-bit signed decimal integer from keyboard
ReadKey – Reads character from keyboard input buffer
ReadString - Reads string from standard input, terminated by [Enter]
SetTextColor - Sets foreground and background colors of all subsequent console text output
Str_compare – Compares two strings
Str_copy – Copies a source string to a destination string
StrLength – Returns length of a string
Str_trim - Removes unwanted characters from a string.

## Slide 44: Irvine32 Procedures - Overview (4 of 5)
Str_ucase - Converts a string to uppercase letters.
WaitMsg - Displays message, waits for Enter key to be pressed
WriteBin - Writes unsigned 32-bit integer in ASCII binary format.
WriteBinB – Writes binary integer in byte, word, or doubleword format
WriteChar - Writes a single character to standard output
WriteDec - Writes unsigned 32-bit integer in decimal format
WriteHex - Writes an unsigned 32-bit integer in hexadecimal format
WriteHexB – Writes byte, word, or doubleword in hexadecimal format
WriteInt - Writes signed 32-bit integer in decimal format

## Slide 45: Irvine32 Procedures - Overview (5 of 5)
WriteStackFrame - Writes the current procedure’s stack frame to the console.
WriteStackFrameName - Writes the current procedure’s name and stack frame to the console.
WriteString - Writes null-terminated string to console window
WriteToFile - Writes buffer to output file
WriteWindowsMsg - Displays most recent error message generated by MS-Windows
Download the IrvineLibHelp.exe file by clicking on “Supplemental Files” at
    http://www.kipirvine.com/asm/.
Some other information (we will use later) at
    IrvineLibHelp.chm

## Slide 46: Example 1
.code
call Clrscr
mov eax,500 ; delay value must be in EAX
call Delay
call DumpRegs
Clear the screen, delay the program for 500 milliseconds, and dump the registers and flags.
EAX=00000613 EBX=00000000 ECX=000000FF EDX=00000000
ESI=00000000 EDI=00000100 EBP=0000091E ESP=000000F6
EIP=00401026 EFL=00000286 CF=0 SF=1 ZF=0 OF=0
Sample output:

## Slide 47: Example 2
.data
str1 BYTE "Assembly language is easy!",0
.code
mov edx,OFFSET str1 ; address of the string must be in EDX
call WriteString
call Crlf
Display a null-terminated string and move the cursor to the beginning of the next screen line.

## Slide 48: Example 2a
.data
str1 BYTE "Assembly language is easy!",0Dh,0Ah,0
.code
mov edx,OFFSET str1
call WriteString
Display a null-terminated string and move the cursor to the beginning of the next screen line (use embedded CR/LF)

## Slide 49: Example 3
IntVal = 35
.code
mov eax,IntVal ; value to display must be in EAX
call WriteBin ; display binary
call Crlf
call WriteDec ; display decimal
call Crlf
call WriteHex ; display hexadecimal
call Crlf
Display an unsigned integer in binary, decimal, and hexadecimal, each on a separate line.
0000 0000 0000 0000 0000 0000 0010 0011
35
23
Sample output:

## Slide 50: Example 4
.data
str1 BYTE 80 DUP(0)
.code
mov edx,OFFSET str1 ; address of string must be in EDX
mov ecx,SIZEOF str1 – 1 ; string length must be in ECX
; 79 characters + null byte
call ReadString
Input a string from the user. EDX points to the string and ECX specifies the maximum number of characters the user is permitted to enter.
A null byte is automatically appended to the string.

## Slide 51: Example 5
.code
mov ecx,10 ; loop counter
L1: mov eax,100 ; ceiling value
; value to display must be in EAX
call RandomRange ; generate random int
call WriteInt ; display signed int
call Crlf ; goto next display line
loop L1 ; repeat loop
Generate and display ten pseudorandom signed integers in the range 0 – 99. Pass each integer to WriteInt in EAX and display it on a separate line.

## Slide 52: Example 6
.data
str1 BYTE "Color output is easy!",0
.code
mov eax,yellow + (blue * 16) ; color attr. must be in EAX
call SetTextColor
mov edx,OFFSET str1
call WriteString
call Crlf
Display a null-terminated string with yellow characters on a blue background.
The background color is multiplied by 16 before being added to the foreground color. See the predefined color constants on page 147.
Color attribute = foreground_color + (background_color × 16).

## Slide 53: Example 7: Case Conversion – ReadChar then Convert
TITLE Read then Convert (ReadConv.asm)
; This program reads a lowercase character then convert it to uppercase
INCLUDE Irvine32.inc
.data
msg1 BYTE "Enter a lower case letter: ",0
msg2 BYTE 'In upper case it is: '
char BYTE ?,0
.code
main PROC
mov edx, OFFSET msg1
CALL WriteString
CALL ReadChar ; read character is always returned in AL
sub al, 20h ; converts to uppercase letter
mov char, al
mov edx, OFFSET msg2
CALL WriteString
exit
  main ENDP
    END main

## Slide 54: Exercise 4
Rval DWORD ?
Xval DWORD 26
Yval DWORD 30
Zval DWORD 40
.code
mov eax,Xval
neg eax ; EAX = -26
mov ebx,Yval
sub ebx,Zval ; EBX = -10
add eax,ebx
mov Rval,eax ; -36
The code below implements the following expression into assembler. Write a full program that read in the values of Xval, Yval and Zval, and then 1) display their values in a single line, 2) display the result in the following line, and 3) display the contents of the general purpose registers in following lines.
Rval = -Xval + (Yval – Zval)

## Slide 55: Exercise 5
mov ebx,Yval
neg ebx
add ebx,Zval
mov eax,Xval
sub eax,ebx
mov Rval,eax
Translate the following expression into assembly language. Do not permit Xval, Yval, or Zval to be modified:
Rval = Xval - (-Yval + Zval)
Assume that all values are signed doublewords.

## Slide 56: 46 69 6E 61 6C