## Slide 1: Assembly Language for x86 Processors 6th Edition
Chapter 4: Data-Related Operators and Directives, Addressing Modes
(c) Pearson Education, 2010. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Slides prepared by the author
Revision date: 2/15/2010
Kip Irvine

## Slide 2: Addressing Modes
Operands specify the data to be used by an instruction
An addressing mode refers to the way in which the data is specified by an operand
  An operand is said to be direct when it specifies directly the data to be used by the instruction. This is the case for imm, reg, and mem operands (see previous chapters)
  An operand is said to be indirect when it specifies the address (in virtual memory) of the data to be used by the instruction
To specify to the assembler that an operand is indirect we enclose it between […]
Indirect addressing is a necessity when we want to manipulate values that are stored in large arrays because we need then an operand that can index (and run along) the array
  Ex: to compute an average of values

## Slide 3: Indirect Addressing
When a register contains the address of the value that we want to use for an instruction, we can provide [reg] for the operand
  This is called register indirect addressing
  The register must be 32 bits wide because offset addresses are on 32 bits. Hence, we must use either EAX, EBX, ECX, EDX, ESI, EDI, ESP, EBP
Ex: Suppose that the double word located at address 100h contains 37A68AF2h.
  If ESI contains 100h, the next instruction will load EAX with the double word dwVar located at address 100h:
    mov eax,[esi] ; EAX=37A68AF2h (indirect addressing)
    ; ESI = 100h and EAX = *ESI
  In contrast, the next instruction will load EAX with the double word contained in ESI:
    mov eax, esi ; EAX = 100h (direct addressing)

## Slide 4: Getting the Address of a Memory Location
To use indirect register addressing we need a way to load a register with the address of a memory location
For this we can use the OFFSET operator. The next instruction loads EAX with the offset address of the memory location named “result”
    .data
    result DWORD 25
    .code
    mov eax, OFFSET result; EAX = &Result
    ;EAX now contains the offset address of result
We can also use the LEA (load effective address) instruction to perform the same task. Except, LEA can obtain an address calculated at runtime
    lea eax, result; EAX = &Result
    ;EAX now contains the offset address of result
In contrast, the following transfers the content of the operand
    mov eax, result ; EAX = 25
Skip to Page 8

## Slide 5: OFFSET Operator
OFFSET returns the distance in bytes, of a label from the beginning of its enclosing (code, data, stack, …) segment
  Protected mode: 32 bits virtual address
  Real mode: 16 bits virtual address
The Protected-mode programs we write use only a single segment (flat memory model).

## Slide 6: OFFSET Examples
.data
bVal BYTE ?
wVal WORD ?
dVal DWORD ?
dVal2 DWORD ?
.code
mov esi,OFFSET bVal ; ESI = 00404000
mov esi,OFFSET wVal ; ESI = 00404001
mov esi,OFFSET dVal ; ESI = 00404003
mov esi,OFFSET dVal2 ; ESI = 00404007
Let's assume that the data segment begins at 00404000h:
OFFSET returns the address of the variable
Thus ESI is a pointer to the variable

## Slide 7: Relating to C/C++
// C++ version:
char array[1000];
char * p = array;
The value returned by OFFSET is a pointer. Compare the following code written for both C++ and assembly language:
; Assembly language:
.data
array BYTE 1000 DUP(?)
.code
mov esi,OFFSET array

## Slide 8: Indirect Operands (1 of 2)
.data
val1 BYTE 10h,20h,30h
.code
mov esi,OFFSET val1 ; ESI = &val1 (in C/C++/Java)
mov al,[esi] ; dereference ESI (AL = 10h)
inc esi
mov al,[esi] ; AL = 20h
inc esi
mov al,[esi] ; AL = 30h
An indirect operand holds the address of a variable, usually an array or string. It can be dereferenced (just like a pointer).
  A pointer variable (mem or reg) is a variable (mem or reg) containing an address as value

## Slide 9: The Type of an Indirect Operand
The type of an indirect operand is determined by the assembler when it is used in an instruction that needs two operands of the same type.
    mov eax, [ebx] ;a double word is moved
    mov ax, [ebx] ;a word is moved
    mov [ebx], ah ;a byte is moved
However, in some cases, the assembler cannot determine the type.
    mov [eax],1 ;error
  Indeed, how many bytes should be moved at the address contained in EAX?
  Sould we move 01h? or 0001h? or 00000001h ?? Here we need to specify explicitly the type to the assembler
The PTR operator forces the type of an operand. Hence:
    mov byte ptr [eax], 1 ;moves 01h
    mov word ptr [eax], 1 ;moves 0001h
    mov dword ptr [eax], 1 ;moves 00000001h
    mov qword ptr [eax], 1 ;error, illegal op. size

## Slide 10: Indirect Operands (2 of 2)
.data
myCount WORD 0
.code
mov esi,OFFSET myCount
inc [esi] ; error: ambiguous
inc WORD PTR [esi] ; ok
Use PTR to clarify the size attribute of a memory operand.
Skip to Page 17
Should PTR be used here?
add [esi],20
yes, because [esi] could point to a byte, word, or doubleword

## Slide 11: PTR Operator
.data
myDouble DWORD 12345678h
.code
mov ax,myDouble ; error – why?
mov ax,WORD PTR myDouble ; loads 5678h
mov WORD PTR myDouble,4321h ; saves 4321h
Overrides the default type of a label (variable). Provides the flexibility to access part of a variable.
Similar to type casting in C/C++ or Java
Little endian order is used when storing data in memory (see Section 3.4.9).

## Slide 12: Little Endian Order
Little endian order refers to the way Intel stores integers in memory.
Multi-byte integers are stored in reverse order, with the least significant byte stored at the lowest address
For example, the doubleword 12345678h would be stored as:
When integers are loaded from memory into registers, the bytes are automatically re-reversed into their correct positions.

## Slide 13: PTR Operator Examples
.data
myDouble DWORD 12345678h
mov al,BYTE PTR myDouble ; AL = 78h
mov al,BYTE PTR [myDouble+1] ; AL = 56h
mov al,BYTE PTR [myDouble+2] ; AL = 34h
mov ax,WORD PTR myDouble ; AX = 5678h
mov ax,WORD PTR [myDouble+2] ; AX = 1234h

## Slide 14: PTR Operator (cont)
.data
myBytes BYTE 12h,34h,56h,78h
.code
mov ax,WORD PTR [myBytes] ; AX = 3412h
mov ax,WORD PTR [myBytes+2] ; AX = 7856h
mov eax,DWORD PTR myBytes ; EAX = 78563412h
PTR can also be used to combine elements of a smaller data type and move them into a larger operand. The CPU will automatically reverse the bytes.

## Slide 15: Your turn . . .
.data
varB BYTE 65h,31h,02h,05h
varW WORD 6543h,1202h
varD DWORD 12345678h
.code
mov ax,WORD PTR [varB+2] ; a.
mov bl,BYTE PTR varD ; b.
mov bl,BYTE PTR [varW+2] ; c.
mov ax,WORD PTR [varD+2] ; d.
mov eax,DWORD PTR varW ; e.
Write down the value of each destination operand:
0502h
78h
02h
1234h
12026543h

## Slide 16: Array Sum Example
.data
arrayW WORD 1000h,2000h,3000h
.code
  mov esi,OFFSET arrayW
  mov ax,[esi]
  add esi,2 ; or: add esi,TYPE arrayW
  add ax,[esi]
  add esi,2
  add ax,[esi] ; AX = sum of the array
Indirect operands are ideal for traversing an array. Note that the register in brackets must be incremented by a value that matches the array type.
ToDo: Modify this example for an array of doublewords.

## Slide 17: Ex: Summing the Elements of an Array
EAX holds the sum
ECX holds nb of elements in arr
Register EBX holds address of the current double word element
  We say that EBX points to the current double word
ADD EAX, [EBX] increases EAX by the number pointed by EBX
When EBX is increased by 4, it points to the next double word
The sum is printed by call WriteDec
INCLUDE Irvine32.inc
.data
arr DWORD 10,23,45,3,37,66
count DWORD 6 ; arr size
.code
main PROC
mov eax, 0 ; holds the sum
mov ecx, count
mov ebx, OFFSET arr
next:
add eax,[ebx]
add ebx,4
loop next
call WriteDec
exit
main ENDP
END main

## Slide 18: Indexed Operands
.data
arrayW WORD 1000h,2000h,3000h
.code
mov esi,0
mov ax,[arrayW + esi] ; AX = 1000h
mov ax,arrayW[esi] ; alternate format
add esi,2
add ax,[arrayW + esi]
etc.
An indexed operand adds a constant to a register to generate an effective address. There are two notational forms:
[label + reg] label[reg]
Where, label is either variable name or an integer
ToDo: Modify this example for an array of doublewords.

## Slide 19: Indexed Operands
Examples:
    .data
    A WORD 10,20,30,40,50,60
    .code
    mov ebp, offset A
    mov esi, 2
    mov ax, [ebp+4] ;AX = 30
    mov ax, 4[ebp] ;same as above
    mov ax, [esi+A] ;AX = 20
    mov ax, A[esi] ;same as above
    mov ax, A[esi+4] ;AX = 40
    Mov ax, [esi-2+A];AX = 10
We can also multiply by 1, 2, 4, or 8. Ex:
    mov ax, A[esi*2+2] ;AX = 40
    This is called index scaling

## Slide 20: Index Scaling
.data
arrayB BYTE 0,1,2,3,4,5
arrayW WORD 0,1,2,3,4,5
arrayD DWORD 0,1,2,3,4,5
.code
mov esi,4
mov al,arrayB[esi*TYPE arrayB] ; 04
mov bx,arrayW[esi*TYPE arrayW] ; 0004
mov edx,arrayD[esi*TYPE arrayD] ; 00000004
You can scale an indirect or indexed operand to the offset of an array element. This is done by multiplying the index by the array's TYPE:

## Slide 21: TYPE Operator
The TYPE operator returns the size, in bytes, of a single element of a data declaration.
Number of bytes in a single variable
.data
var1 BYTE ?
var2 WORD ?
var3 DWORD ?
var4 QWORD ?
.code
mov eax,TYPE var1 ; 1
mov eax,TYPE var2 ; 2
mov eax,TYPE var3 ; 4
mov eax,TYPE var4 ; 8

## Slide 22: Using Indexed Operands and Scaling
This is the same program as before for summing the elements of an array
Except that the loop now contains only this instruction
    add ebx,arr[(ecx-1)*4]
It uses indexed operand with a scaling factor
It should be more efficient than the previous program
INCLUDE Irvine32.inc
.data
arr DWORD 10,23,45,3,37,66
count DWORD 6 ;size of arr
.code
main PROC
mov eax, 0 ; holds the sum
mov ecx, count
next:
add eax, arr[(ecx-1)*4]
loop next
call WriteDec
exit
main ENDP
END main

## Slide 23: Indirect Addressing with Two Registers*
We can also use two registers. Ex:
    .data
    A BYTE 10,20,30,40,50,60
    .code
    mov eax, 2
    mov ebx, 3
    mov dh, [A+eax+ebx] ;DH = 60
    mov dh, A[eax+ebx] ;same as above
    mov dh, A[eax][ebx] ;same as above
A two-dimensional array example:
    .data
    arr BYTE 10h, 20h, 30h
    BYTE 0Ah, 0Bh, 0Ch
    .code
    mov ebx, 3 ;choose 2nd row
    mov esi, 2 ;choose 3rd column
    mov al, arr[ebx][esi] ;AL = 0Ch
    add ebx, offset arr ;EBX = address of arr+3
    mov ah, [ebx][esi] ;AH = 0Ch

## Slide 24: Pointers
.data
arrayW WORD 1000h,2000h,3000h
ptrW DWORD arrayW ; int ptrW *arrayW
.code
mov esi,ptrW
mov ax,[esi] ; AX = 1000h
You can declare a pointer variable that contains the offset of another variable.
Alternate format:
ptrW DWORD OFFSET arrayW

## Slide 25: LENGTHOF Operator
.data LENGTHOF
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 32
array2 WORD 5 DUP(3 DUP(?)) ; 15
array3 DWORD 1,2,3,4 ; 4
digitStr BYTE "12345678",0 ; 9
.code
mov ecx,LENGTHOF array1 ; 32
The LENGTHOF operator counts the number of elements in a single data declaration.
Number of elements in an array variable

## Slide 26: SIZEOF Operator
.data SIZEOF
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 64
array2 WORD 5 DUP(3 DUP(?)) ; 30
array3 DWORD 1,2,3,4 ; 16
digitStr BYTE "12345678",0 ; 9
.code
mov ecx,SIZEOF array1 ; 64
The SIZEOF operator returns a value that is equivalent to multiplying LENGTHOF by TYPE.
Number of bytes in an array variable
Skip to Page 29

## Slide 27: Spanning Multiple Lines (1 of 2)
.data
array WORD 10,20,
30,40,
50,60
.code
mov eax,LENGTHOF array ; 6
mov ebx,SIZEOF array ; 12
A data declaration spans multiple lines if each line (except the last) ends with a comma. The LENGTHOF and SIZEOF operators include all lines belonging to the declaration:

## Slide 28: Spanning Multiple Lines (2 of 2)
.data
array WORD 10,20
WORD 30,40
WORD 50,60
.code
mov eax,LENGTHOF array ; 2
mov ebx,SIZEOF array ; 4
In the following example, array identifies only the first WORD declaration. Compare the values returned by LENGTHOF and SIZEOF here to those in the previous slide:

## Slide 29: Summing an Integer Array (Using Data-Related Operators and Directives)
.data
intarray WORD 100h,200h,300h,400h
.code
  mov edi,OFFSET intarray ; address of intarray
  mov ecx,LENGTHOF intarray ; loop counter
  mov ax,0 ; zero the accumulator
L1:
  add ax,[edi] ; add an integer
  add edi,TYPE intarray ; point to next integer
loop L1 ; repeat until ECX = 0
The following code calculates the sum of an array of 16-bit integers.

## Slide 30: Copying a String
.data
source BYTE "This is the source string",0
target BYTE SIZEOF source DUP(0)
.code
mov esi,0 ; index register
mov ecx,SIZEOF source ; loop counter
L1:
mov al,source[esi] ; get char from source
mov target[esi],al ; store it in the target
inc esi ; move to next character
loop L1 ; repeat for entire string
good use of SIZEOF
The following code copies a string from source to target:

## Slide 31: Your turn . . .
Rewrite the program shown in the previous slide, using indirect addressing rather than indexed addressing.

## Slide 32: LABEL Directive
Assigns an alternate label name and type to an existing storage location. That is, aliasing.
LABEL does not allocate any storage of its own
Removes the need for the PTR operator
Thus, dwList and wordList are variables without memory allocation, and can be used as any other variable.
.data
dwList LABEL DWORD
wordList LABEL WORD
intList BYTE 00h,10h,00h,20h
.code
mov eax,dwList ; 20001000h
mov cx,wordList ; 1000h
mov dl,intList ; 00h

## Slide 33: The LABEL Directive
It gives a name and a size to an existing storage location. It does not allocate storage.
It must be used in conjunction with byte, word, dword, ...
    .data
    val16 LABEL WORD ;no allocation
    val32 DWORD 12345678h ;allocates storage
    .code
    mov eax,val32 ;EAX = 12345678h
    mov ax,val32 ;error
    mov ax,val16 ;AX = 5678h
val16 is just an alias for the first two bytes of the storage location val32

## Slide 34: Exercise 3
We have the following data segment :
    .data
    YOU WORD 3421h, 5AC6h
    ME DWORD 8AF67B11h
Given that MOV ESI, OFFSET YOU has just been executed, write the hexadecimal content of the destination operand immediately after the execution of each instruction below:
    MOV BH, BYTE PTR [ESI+1] ; BH =
    MOV BH, BYTE PTR [ESI+2] ; BH =
    MOV BX, WORD PTR [ESI+6] ; BX =
    MOV BX, WORD PTR [ESI+1] ; BX =
    MOV EBX, DWORD PTR [ESI+3] ; EBX =

## Slide 35: Exercise 4
Given the data segment
    .DATA
    A WORD 1234H
    B LABEL BYTE
    WORD 5678H
    C LABEL WORD
    C1 BYTE 9AH
    C2 BYTE 0BCH
Tell whether the following instructions are legal, if so give the number moved
    MOV AX, B
    MOV AH, B
    MOV CX, C
    MOV BX, WORD PTR B
    MOV DL, WORD PTR C
    MOV AX, WORD PTR C1
    MOV BX, [C]
    MOV BX, C

## Slide 36: 46 69 6E 61 6C